## Slide 1: NTCNA PCAP Decoder JSON Converter V2.0
Python application to convert PCAP data to JSON format
Now provided in standalone executables for Windows

## Slide 2: The Application

## Slide 3: Using the tool
cd j2735_tools/j2735_decoder
  Linux: j2735_decoder_gui.py &
  Windows: j2735_decoder_gui.cmd (creating a shortcut would help)
Input File(s)
  Select 1 or more PCAP (*.pcap, *.pcapng) files to decode and convert
    Cohda, Commsignia, DENSO, Panasonic, Savari, Wistron OBU formats
    0x88DC special, Linux cooked, Radiotap and Tazman formats supported
    RSU TSCBM and IFM formats (CI and CTIC projects)
  eTrans tool *.log files (not Kapsch *.csv files)
    Decodes hex data
Output Dir
  Select base output directory for JSON files (default “logs”)
  Basename is root filename of input file, will replace spaces with underscores in name
  Output directory format: logs/basename/files.json, …
Convert File(s)
  Starts conversion process on selected file(s)
  Leaves behind metadata.txt file with conversion details
  Optional debug.txt with record by record details
Exit
  Quit program

## Slide 4: Tool options
Debug Log
  Output detailed conversion log to debug.txt file
Output Binary MAPs
  Extracts J2735 UPER encoded MAPs to binary files (.bin)
Output MAPs/SPATs into file (combined)
  mapspat-reg#-id#.json
Separate MAPs/SPATs into files (split)
  map-reg#-id#.json
  spat-reg#-id#.json
Split BSMs into files by Id
  By CAMP ID (lower 2 bytes only)
  bsm-id#.json
BSM Conversion of split files
  Split files only
  Converts BSM data from raw values to engineering unit values

## Slide 5: Command line version
For the convenience of mass converting files
Output files into log output directory
./j2735_decoder.py [options] <files>
Python3 J2735-2024-05-28 PCAP Decoder V2.0.4 j2735_decoder.py bcdhmo:su:v:BO: <input PCAP files> -b Split BSMs to file by ID -c Converting BSM enabled -d Debugging enabled to debug.txt -h Help -m Binary MAP output in J2735 UPER format -o <offs> UDP offset to data in bytes -s Split MAPs/SPATs to file by ID in JSON -u <port> UDP port -v vid BSMs extracted by vehicle id -B Use PCAP file base name as base path to output directory -O <path> Path to output base directory Creates JSON and KML (MAP) files with metadata.txt to <path>/<base>

## Slide 6: V2X PCAP Recording Rules
Capturing radio data for conversion and analysis

## Slide 7: Standardizing how we capture data
Compatibility with j2735_tools
We are getting different formats from different OBU/RSU radio vendors
  Complicates our efforts, but some vendors have agreed on special 0x88DC PCAP format
PCAP or PCAPng
  Either is fine
Avoid weird encodings of data in PCAP file
  IPv4/IPv6 layer without Ethernet layer
Full radio stack capture (complex)
  DSRC stacks (based on 802.11p), including 1609.3 WSMP layer
  C-V2X stacks
UDP dump of 1609.2 and J2735 data (simpler)
  Write to a normal UDP socket
Once we get to J2735 layer, we can decode it
  Using ASN.1 compiler tools (C/C++/Java/Rust?)
    Output to XML, some tools output JSON
  Using Python3 Pycrate module
    Convert to JSON
  Import JSON into big data science tools like Pandas and/or Anaconda, even Snowflake

## Slide 8: Full Radio Stack Capture (DSRC)
Network Layers | Network Data
Radiotap (optional) | Radio data
802.11 QoS layer | Provides 802.11 information
LLC layer | Indicates WSMP layer (0x88dc)
WSMP layer | WSMP –N header, –T header and message:
1609.2 layer | Security signage (even if unsigned)
J2735 layer | BSM, MAP, SPAT, RTCM, …
Captured at network interface
  Using tcpdump, wireshark or similar tool
PCAP contents can be forwarded over UDP
  Receiver application writes data to PCAP file
Add Radiotap layer for radio information to help debug radio
Please do not write hand coded PCAPs that don’t follow the rules
Separating TX and RX data into separate PCAPs makes analysis easier
  Since BSM TempID is randomized

## Slide 9: Full Radio Stack Capture (C-V2X)
Network Layers | Network Data
Radiotap (optional) | Radio data
TBD | TBD
TBD | TBD
TBD | TBD
1609.2 layer | Security signage (even if unsigned)
J2735 layer | BSM, MAP, SPAT, RTCM, …
Some OBUs send over UDP (Cohda ports 9000-9001)
Or use special 0x88DC format for OTA data
Same rules as for DSRC, needs WSMP layer

## Slide 10: UDP V2X Stack Capture (C-V2X or DSRC)
Network Layers | Network Data
Ethernet frame | Ethernet data
IPv4 or IPv6 6 layer | TCP/IP layer
UDP layer | Standard UDP sockets
1609.2 layer | Security signage (even if unsigned)
J2735 layer | BSM, MAP, SPAT, RTCM, …
C-V2X and DSRC agnostic
Doesn’t provide 802.11 or WSMP layers which are DSRC specific
Open UDP socket to destination and write data:
Includes both 1609.2 and J2735 layers
Can’t distinguish TX from RX?
  Use different UDP ports for TX and RX

## Slide 11: UDP V2X Stack Capture (DSRC) Tazman
Network Layers | Network Data
Ethernet Frame | Ethernet packet
IPv4 or IPv6 6 layer | TCP/IP layer
UDP layer | Standard UDP socket on port 37008
Tazman Sniffer Layer (optional) | Radio data
WSMP layer | WSMP –N header –T header message
1609.2 layer | Security signage (even if unsigned)
J2735 layer | BSM, MAP, SPAT, RTCM, …
Same UDP rules as above
802.11 specific
Tazman layer adds additional radio information
  Some information is redundant with WSMP, helps when WSMP is not present
Last ditch looks for 0x88DC signature for WSMP

## Slide 12: The Gory Details
Python 3
  Python 3.11 or greater (Python 2 is EOL)
  PySide6 or higher for QT6 based GUI (multiplatform)
    Uses Qt Creator to edit the .ui files
    The pyside6-uic mainwindow.ui –o MainWindow.py generates code
Network packet dissection
  Python package scapy (https://scapy.net/)
Packet Decoding
  Uses the Python package Pycrate (https://github.com/P1sec/pycrate)
    python –m pip install pycrate
  Uses Pycreate to decode J2735 ASN.1 UPER
  1609.2 ASN.1 OER is manually decoded

## Slide 13: The CAMP/TOSCo/CI/CTIC JSON Format for J2735
100% JSON and easy to parse using Python’s json package.
Header example:
{"Timestamp":1597167252195,"Direction":"RX","Message_id":19,"P1609dot2_flag":0,"Message":{"messageId":19,"value":{...}},"Version":"1.0”}
Header fields
  Timestamp is milliseconds since the Epoch (Jan 1st 1970), 13 digits
  Direction indicates if message is TX or RX
  Message_id is the J2735 messageID [MAP=18, SPAT=19, BSM=20, …]
  P1609dot2_flag if set, indicates if message was unsigned(0) or signed(1)
  Version is included on 1st record only
  Conversion (not seen) is added for BSMs with converted data
  Message field gives J2735 data structure as decoded to JSON
Samples
  Don’t copy from document because PowerPoint formats them funny (line wrapping on hyphens)
Import JSON into big data science tools like Pandas and/or Anaconda
  Pandas
  Anaconda
  Snowflake
  …

## Slide 14: MAP sample
{"Timestamp":1597167253960,"Direction":"RX","Message_id":18,"P1609dot2_flag":0,"Message":{"messageId":18,"value":{"intersections":[{"id":{"id":782},"laneSet":[{"connectsTo":[{"connectingLane":{"lane":11 ,"maneuver":"2000"},"signalGroup":2}],"laneAttributes":{"directionalUse":"80","laneType":{"vehicle":" 00"},"sharedWith":"1000"},"laneID":1,"maneuvers":"8000","nodeList":{"nodes":[{"delta":{"node-XY4":{"x ":2083,"y":-2129}}},{"delta":{"node-XY4":{"x":311,"y":-2532}}},{"delta":{"node-XY4":{"x":346,"y":-302 8}}},{"delta":{"node-XY1":{"x":0,"y":-305}}},{"delta":{"node-XY4":{"x":-122,"y":-2659}}}]}},{"connect sTo":[{"connectingLane":{"lane":7,"maneuver":"8000"},"signalGroup":2}],"laneAttributes":{"directional Use":"80","laneType":{"vehicle":"00"},"sharedWith":"1000"},"laneID":2,"maneuvers":"8000","nodeList":{ "nodes":[{"delta":{"node-XY4":{"x":638,"y":-2316}}},{"delta":{"node-XY4":{"x":337,"y":-2788}}},{"delt a":{"node-XY4":{"x":284,"y":-2729}}},{"delta":{"node-XY4":{"x":246,"y":-2732}}},{"delta":{"node-XY4": {"x":241,"y":-3344}}},{"delta":{"node-XY4":{"x":149,"y":-2739}}},{"delta":{"node-XY3":{"x":74,"y":-18 27}}},{"delta":{"node-XY6":{"x":352,"y":-11273}}}]}},{"connectsTo":[{"connectingLane":{"lane":8,"mane uver":"8000"},"signalGroup":2}],"laneAttributes":{"directionalUse":"80","laneType":{"vehicle":"00"}," sharedWith":"1000"},"laneID":3,"maneuvers":"8000","nodeList":{"nodes":[{"delta":{"node-XY4":{"x":998, "y":-2270}}},{"delta":{"node-XY4":{"x":309,"y":-2533}}},{"delta":{"node-XY4":{"x":322,"y":-3031}}},{" delta":{"node-XY4":{"x":244,"y":-2732}}},{"delta":{"node-XY4":{"x":242,"y":-3344}}},{"delta":{"node-X Y4":{"x":145,"y":-2739}}},{"delta":{"node-XY3":{"x":61,"y":-1523}}},{"delta":{"node-XY6":{"x":359,"y" :-11578}}}]}},{"connectsTo":[{"connectingLane":{"lane":9,"maneuver":"8000"},"signalGroup":2}],"laneAt tributes":{"directionalUse":"80","laneType":{"vehicle":"00"},"sharedWith":"1000"},"laneID":4,"maneuve rs":"8000","nodeList":{"nodes":[{"delta":{"node-XY4":{"x":1362,"y":-2222}}},{"delta":{"node-XY4":{"x" :319,"y":-2590}}},{"delta":{"node-XY4":{"x":322,"y":-3031}}},{"delta":{"node-XY4":{"x":242,"y":-2733} }},{"delta":{"node-XY4":{"x":242,"y":-3344}}},{"delta":{"node-XY4":{"x":146,"y":-2739}}},{"delta":{"n ode-XY3":{"x":51,"y":-1218}}},{"delta":{"node-XY6":{"x":366,"y":-11882}}}]}},{"connectsTo":[{"connect ingLane":{"lane":10,"maneuver":"8000"},"signalGroup":2}],"laneAttributes":{"directionalUse":"80","lan eType":{"vehicle":"00"},"sharedWith":"1000"},"laneID":5,"maneuvers":"8000","nodeList":{"nodes":[{"del ta":{"node-XY4":{"x":1724,"y":-2175}}},{"delta":{"node-XY4":{"x":324,"y":-2643}}},{"delta":{"node-XY4 ":{"x":321,"y":-3031}}},{"delta":{"node-XY4":{"x":270,"y":-3036}}},{"delta":{"node-XY4":{"x":215,"y": -3041}}},{"delta":{"node-XY4":{"x":148,"y":-2739}}},{"delta":{"node-XY3":{"x":73,"y":-1827}}},{"delta ":{"node-XY6":{"x":344,"y":-11273}}}]}},{"connectsTo":[{"connectingLane":{"lane":7,"maneuver":"4000"} ,"signalGroup":4}],"laneAttributes":{"directionalUse":"80","laneType":{"vehicle":"00"},"sharedWith":" 1000"},"laneID":6,"maneuvers":"4000","nodeList":{"nodes":[{"delta":{"node-XY2":{"x":-130,"y":-899}}}, {"delta":{"node-XY1":{"x":-296,"y":-72}}},{"delta":{"node-XY1":{"x":-303,"y":-14}}},{"delta":{"node-X Y1":{"x":-292,"y":69}}},{"delta":{"node-XY1":{"x":-225,"y":204}}},{"delta":{"node-XY1":{"x":-170,"y": 251}}},{"delta":{"node-XY1":{"x":-128,"y":276}}},{"delta":{"node-XY1":{"x":-100,"y":287}}},{"delta":{ "node-XY2":{"x":-151,"y":590}}},{"delta":{"node-XY1":{"x":-58,"y":299}}},{"delta":{"node-XY3":{"x":-2 35,"y":1814}}},{"delta":{"node-XY4":{"x":-371,"y":3332}}},{"delta":{"node-XY4":{"x":-310,"y":3339}}}, {"delta":{"node-XY4":{"x":-256,"y":3343}}},{"delta":{"node-XY4":{"x":-561,"y":3973}}}]}},{"laneAttrib utes":{"directionalUse":"40","laneType":{"vehicle":"00"},"sharedWith":"1000"},"laneID":7,"nodeList":{ "nodes":[{"delta":{"node-XY2":{"x":268,"y":470}}},{"delta":{"node-XY4":{"x":-312,"y":2419}}},{"delta" :{"node-XY3":{"x":-215,"y":1816}}},{"delta":{"node-XY4":{"x":-253,"y":2425}}},{"delta":{"node-XY4":{" x":-248,"y":2732}}}]}},{"laneAttributes":{"directionalUse":"40","laneType":{"vehicle":"00"},"sharedWi th":"1000"},"laneID":8,"nodeList":{"nodes":[{"delta":{"node-XY2":{"x":626,"y":522}}},{"delta":{"node- XY4":{"x":-494,"y":3932}}},{"delta":{"node-XY4":{"x":-287,"y":2728}}},{"delta":{"node-XY4":{"x":-247, "y":2732}}}]}},{"laneAttributes":{"directionalUse":"40","laneType":{"vehicle":"00"},"sharedWith":"100 0"},"laneID":9,"nodeList":{"nodes":[{"delta":{"node-XY3":{"x":988,"y":575}}},{"delta":{"node-XY4":{"x ":-314,"y":2418}}},{"delta":{"node-XY4":{"x":-312,"y":2726}}},{"delta":{"node-LatLon":{"lat":42519651 3,"lon":-830469748}}},{"delta":{"node-XY4":{"x":-217,"y":2429}}}]}},{"laneAttributes":{"directionalUs e":"40","laneType":{"vehicle":"00"},"sharedWith":"1000"},"laneID":10,"nodeList":{"nodes":[{"delta":{" node-XY3":{"x":1352,"y":628}}},{"delta":{"node-XY4":{"x":-315,"y":2418}}},{"delta":{"node-XY4":{"x":- 281,"y":2415}}},{"delta":{"node-XY3":{"x":-188,"y":1819}}},{"delta":{"node-LatLon":{"lat":425199014," lon":-830469603}}}]}},{"laneAttributes":{"directionalUse":"40","laneType":{"vehicle":"00"},"sharedWit h":"1000"},"laneID":11,"nodeList":{"nodes":[{"delta":{"node-XY3":{"x":1712,"y":681}}},{"delta":{"node -XY4":{"x":-276,"y":2116}}},{"delta":{"node-XY4":{"x":-349,"y":3028}}},{"delta":{"node-XY3":{"x":-155 ,"y":1516}}},{"delta":{"node-LatLon":{"lat":425199067,"lon":-830469158}}}]}}],"laneWidth":366,"refPoi nt":{"elevation":1879,"lat":425190000,"long":-830470000},"revision":1}],"layerID":1,"layerType":"inte rsectionData","msgIssueRevision":1}}}

## Slide 15: SPAT sample
{"Timestamp":1597167252195,"Direction":"RX","Message_id":19,"P1609dot2_flag":0,"Message":{"messageId" :19,"value":{"intersections":[{"id":{"id":782},"revision":4,"states":[{"signalGroup":1,"state-time-sp eed":[{"eventState":"stop-And-Remain","timing":{"maxEndTime":20294,"minEndTime":36001}}]},{"signalGro up":2,"state-time-speed":[{"eventState":"stop-And-Remain","timing":{"maxEndTime":20603,"minEndTime":2 0603}}]},{"signalGroup":3,"state-time-speed":[{"eventState":"stop-And-Remain","timing":{"maxEndTime": 20294,"minEndTime":36001}}]},{"signalGroup":4,"state-time-speed":[{"eventState":"permissive-Movement- Allowed","timing":{"maxEndTime":20545,"minEndTime":20545}}]},{"signalGroup":6,"state-time-speed":[{"e ventState":"stop-And-Remain","timing":{"maxEndTime":20294,"minEndTime":36001}}]},{"signalGroup":7,"st ate-time-speed":[{"eventState":"stop-And-Remain","timing":{"maxEndTime":20294,"minEndTime":36001}}]}, {"signalGroup":8,"state-time-speed":[{"eventState":"stop-And-Remain","timing":{"maxEndTime":20294,"mi nEndTime":36001}}]}],"status":"0080"}]}},"Version":"1.0"}

## Slide 16: BSM sample
{"Timestamp":1602096334182,"Direction":"RX","Message_id":20,"P1609dot2_flag":0,"Message":{"messageId":20,"value":{"coreData":{"accelSet":{"lat":-7,"long":24,"vert":-127,"yaw":-40},"accuracy":{"orientation":0,"semiMajor":5,"semiMinor":5},"angle":28,"brakes":{"abs":"engaged","auxBrakes":"unavailable","brakeBoost":"unavailable","scs":"engaged","traction":"engaged","wheelBrakes":"00"},"elev":1508,"heading ":1993,"id":"06230106","lat":425686803,"long":-829123338,"msgCnt":110,"secMark":34100,"size":{"length ":504,"width":196},"speed":0,"transmission":"park"},"partII":[{"partII-Id":0,"partII-Value":{"pathHis tory":{"crumbData":[{"elevationOffset":5,"latOffset":930,"lonOffset":742,"timeOffset":2230},{"elevati onOffset":9,"latOffset":930,"lonOffset":2164,"timeOffset":2610},{"elevationOffset":11,"latOffset":123 6,"lonOffset":2917,"timeOffset":2760},{"elevationOffset":11,"latOffset":8992,"lonOffset":9400,"timeOf fset":3600},{"elevationOffset":8,"latOffset":25129,"lonOffset":21801,"timeOffset":4780}]},"pathPredic tion":{"confidence":200,"radiusOfCurve":32767}}}]}},"Version":"1.0"}

## Slide 17: Installing

## Slide 18: Python 3 Packages
Python is part of Linux and Raspberry Pi, already installed
Windows
  Download and install from https://www.python.org/downloads/
Packages
  Pycrate, Pyside2, Scapy, …

## Slide 19: Linux Installation
Run ./setup.sh script provided
Add classes and classes/j2735 to your PYTHONPATH
  export PYTHONPATH=~/j2735_tools/classes:~/j2735_tools/classes/j2735
  Edit to reflect where you installed the application

## Slide 20: Windows Installation
Use setup.cmd to install everything
Using PowerShell Admin:
  python –m pip install –upgrade pip
  python –m pip install numpy pyside2 scapy pyyaml virtualenv virtualenvwrapper
Installing Pycrate
  Python –m pip install pycrate
  Old method:
    git clone https://github.com/P1sec/pycrate.git
    cd pycrate
    python setup.py install

## Slide 21: Other Tools

## Slide 22: Wireshark
Wireshark-DSRC with J2735 Dissection
  Linux or Windows
  https://github.com/nprobert/Wireshark-J2735