## Slide 1: NTCNA V2 V2X OTA PCAP Format Decoding to JSON
Originally Developed by Nissan NTCNA for CAMP, CI and CTI Projects
Python application to convert PCAP data to JSON format
Neal Probert, Senior Cybersecurity Engineer, Nissan

## Slide 2: Introduction
Work
  The work done to date has been done by me, as part of Nissan for the CAMP and SAE projects including CI and CTI.
  Maintained it mostly for Jay Parikh’s MAP/SPAT Analysis application.
  It’s public because CAMP has disappeared and Nissan doesn’t care.
Baseline
  The DENSO/Cohda protocol is the most common format and while it contains the essential WSMP, 1609.2 and J2735 layers
Plan
  Add the radio details that would be most useful (Radiotap layer)
  Add the Layer 2 information

## Slide 3: V2X PCAP Recording Rules
Capturing radio data for conversion and analysis

## Slide 4: Standardizing how we capture data
We are getting different formats from different OBU/RSU radio vendors
  Complicates our efforts, but some vendors have agreed on (preferred) 0x88DC PCAP format
  Additional formats supported: eTrans, Linux Cooked, Radiotap, Tazman, Mcity TSCBM, RSU IFM, over IPv4/6 UDP
PCAP or PCAPng
  Either is fine and will work
Avoid weird encodings of data in PCAP file
  IPv4/IPv6 layer without Ethernet layer
  Missing 1609.2 layers
Full radio stack capture (complex)
  DSRC stacks (based on 802.11p), including 1609.3 WSMP layer
  C-V2X stacks not supported at this time
Single stream logging
  Need to separate RX and TX streams
UDP dump of 1609.2 and J2735 data (simpler)
  Even if unsigned, include the 1609.2 layer!
Once we get to J2735 layer, we can decode it
  Using ASN.1 compiler tools (C/C++/Java/Python/Rust?), some output to JSON
  Import JSON into big data science tools like Pandas and/or Anaconda, even Snowflake
Useful for both debugging, analysis, and certification

## Slide 5: PCAP 0x88DC Ethertype
Network Layers | Network Data
Ethernet Frame 0x88DC | Ethernet packet
WSMP layer | WSMP –N header –T header message
1609.2 layer | Security signage (even if unsigned)
J2735 layer | BSM, MAP, SPAT, RTCM, …
As used by Cohda and DENSO, preferred format
Contains WSMP, 1609.2 and J2735 layers
Simplest format
Suggest adding Radiotap layer and Layer 2 information

## Slide 6: Full Radio Stack Capture (DSRC)
Network Layers | Network Data
Radiotap (optional) | Radio data
802.11 QoS layer | Provides 802.11 information
LLC layer | Indicates WSMP layer (0x88dc)
WSMP layer | WSMP –N header, –T header and message:
1609.2 layer | Security signage (even if unsigned)
J2735 layer | BSM, MAP, SPAT, RTCM, …
Used by older DSRC based OBUs for CAMP projects
Captured at network interface
  Using tcpdump, wireshark or similar tool
PCAP contents can be forwarded over UDP
  Receiver application writes data to PCAP file
  Add Radiotap layer for radio information to help debug radio
Please do not write hand coded PCAPs that don’t follow the rules
Separating TX and RX data into separate PCAPs makes analysis easier
  Since BSM TempID is randomized

## Slide 7: Full Radio Stack Capture (C-V2X)
Network Layers | Network Data
Radiotap (optional) | Radio data
1609.2 layer | Security signage (even if unsigned)
J2735 layer | BSM, MAP, SPAT, RTCM, …
Some OBUs send over UDP (Cohda ports 9000-9001)
Or use special 0x88DC format for OTA data
Same rules as for DSRC, needs WSMP layer
Not supported by tool

## Slide 8: UDP V2X Stack Capture (C-V2X or DSRC)
Network Layers | Network Data
Ethernet frame | Ethernet data
IPv4 or IPv6 6 layer | TCP/IP layer
UDP layer | Standard UDP sockets
1609.2 layer | Security signage (even if unsigned)
J2735 layer | BSM, MAP, SPAT, RTCM, …
OBU unique
C-V2X and DSRC agnostic
Doesn’t provide 802.11 or WSMP layers which give us more info
Open UDP socket to destination and write data:
Should include all WSMP, 1609.2 and J2735 layers
Can’t distinguish TX from RX?
  Use different UDP ports for TX and RX

## Slide 9: UDP V2X Stack Capture (DSRC) Tazman
Network Layers | Network Data
Ethernet Frame | Ethernet packet
IPv4 or IPv6 6 layer | TCP/IP layer
UDP layer | Standard UDP socket on port 37008
Tazman Sniffer Layer (optional) | Radio data
WSMP layer | WSMP –N header –T header message
1609.2 layer | Security signage (even if unsigned)
J2735 layer | BSM, MAP, SPAT, RTCM, …
OBU Unique
802.11 specific
Tazman layer adds additional radio information
  Some information is redundant with WSMP, helps when WSMP is not present
Last ditch looks for 0x88DC signature for WSMP

## Slide 10: The CAMP/TOSCo/CI/CTIC JSON Format for J2735
100% JSON and easy to parse using Python’s json package.
Header example:
{"Timestamp":1597167252195,"Direction":"RX","Message_id":19,"P1609dot2_flag":0,"Message":{"messageId":19,"value":{...}},"Version":"1.0”}
Header fields
  Timestamp is milliseconds since the Epoch (Jan 1st 1970), 13 digits
  Direction indicates if message is TX or RX
  Message_id is the J2735 messageID [MAP=18, SPAT=19, BSM=20, …]
  P1609dot2_flag if set, indicates if message was unsigned(0) or signed(1)
  Version is included on 1st record only
  Conversion (not seen) is added for BSMs with converted data
  Message field gives J2735 data structure as decoded to JSON
Samples
  Don’t copy from document because PowerPoint formats them funny (line wrapping on hyphens)
Import JSON into big data science tools like Pandas and/or Anaconda
  Pandas
  Anaconda
  Snowflake
  …

## Slide 11: Python and Pycrate
The ease of working in Python makes it all worth using Pycrate
  GitHub - P1sec/pycrate: A Python library to ease the development of encoders and decoders for various protocols and file formats; contains ASN.1 and CSN.1 compilers. · GitHub
Pycrate does J2735 ASN.1 UPER quite well
Close to having 1609.2 OER decoding working
PCAP decoder to JSON converter
    GUI and command line
    Wiki: J2735 Tools - ProbeStar V2X Wiki)
    Github: nprobert/j2735_tools
    Compiled version for windows here: https://v2x.probestar.com/j2735_tools/
      Userid = j2735
      Password = pcap_decoder

## Slide 12: Tool options
Debug Log
  Output detailed conversion log to debug.txt file
Output Binary MAPs
  Extracts J2735 UPER encoded MAPs to binary files (.bin)
Output MAPs/SPATs into file (combined)
  mapspat-reg#-id#.json
Separate MAPs/SPATs into files (split)
  map-reg#-id#.json
  spat-reg#-id#.json
Split BSMs into files by Id
  By CAMP ID (lower 2 bytes only)
  bsm-id#.json
BSM Conversion of split files
  Split files only
  Converts BSM data from raw values to engineering unit values
Selected messages (command line –f option, no spaces in list)
  -f BSM,MAP,SPAT,RTCM

## Slide 13: The GUI Application

## Slide 14: Using the tool
cd j2735_tools/j2735_decoder
  Linux: j2735_decoder_gui.py &
  Windows: j2735_decoder_gui.cmd (creating a shortcut would help)
Input File(s)
  Select 1 or more PCAP (*.pcap, *.pcapng) files to decode and convert
    Cohda, Commsignia, DENSO, Panasonic, Savari, Wistron OBU formats
    0x88DC special, Linux cooked, Radiotap and Tazman formats supported
    RSU TSCBM and IFM formats (CI and CTIC projects)
  eTrans tool *.log files (not Kapsch *.csv files)
    Decodes hex data
Output Dir
  Select base output directory for JSON files (default “logs”)
  Basename is root filename of input file, will replace spaces with underscores in name
  Output directory format: logs/basename/files.json, …
Convert File(s)
  Starts conversion process on selected file(s)
  Leaves behind metadata.txt file with conversion details
  Optional debug.txt with details for each record
Exit
  Quit program

## Slide 15: Command line version
For the convenience of mass converting files
Output files into log output directory
./j2735_decoder.py [options] <files>
Python3 J2735-2024-05-28 PCAP Decoder V2.0.11 j2735_decoder.py bcdf:hmo:su:v:BO:
-b Split BSMs to file by ID
-c Converting BSM enabled
-d Debugging enabled to debug.txt
-f Filter by message name, comma seperated list
-h Help
-m Binary MAP output in J2735 UPER format
-o UDP offset to data in bytes
-s Split MAPs/SPATs to file by ID in JSON
-u UDP port
-v vid BSMs extracted by vehicle id
-B Use PCAP file base name as base path to output directory
-O Path to output base directory
Creates JSON and KML (MAP) files with metadata.txt to /

## Slide 16: Building the Application
Building under Linux or Windows
Private github at https://github.com/nprobert/j2735_tools
Userid: j2735 Password: pcap_decoder

## Slide 17: Linux Installation
Python is part of Linux and Raspberry Pi, already installed
Build/run your own
  Run ./packages.sh script provided
  Add classes and classes/j2735 to your PYTHONPATH
    export PYTHONPATH=~/j2735_tools/classes:~/j2735_tools/classes/j2735
    Edit to reflect where you installed the application

## Slide 18: Windows Installation
Windows
  Download and install from https://www.python.org/downloads/
  Use packages.cmd to install everything
  Use .cmd files to run tools
Pre-built binary (using PyInstaller)
  https://v2x.probestar.com/j2735_tools/
  Looking at using Docker
  Wireshark build with J2735 support included

## Slide 19: The Gory Details
Python 3
  Python 3.11 or greater (Python 2 is EOL)
  PySide6 or higher for QT6 based GUI (multiplatform)
    Uses Qt Creator to edit the .ui files
    The pyside6-uic mainwindow.ui –o MainWindow.py generates code
Network packet dissection
  Python package scapy (https://scapy.net/)
Packet Decoding
  Uses the Python package Pycrate (https://github.com/P1sec/pycrate)
    python –m pip install pycrate
  Uses Pycreate to decode J2735 ASN.1 UPER
  1609.2 ASN.1 OER is manually decoded

## Slide 20: Other Tools

## Slide 21: Wireshark
Wireshark-DSRC with J2735 Dissection
  Built using latest version of Wireshark!
  Linux (Ubuntu and RedHat) or Windows 10/11
  https://github.com/nprobert/Wireshark-J2735
  Doesn’t include J2735 ASN.1 needed
    Which has to be modified to compile correctly
  Caveats
    Doesn’t handle missing 1609.2 layer
    Doesn’t correctly show UPER bits
    Doesn’t show J2735 conversions

## Slide 22: MAP sample
{"Timestamp":1597167253960,"Direction":"RX","Message_id":18,"P1609dot2_flag":0,"Message":{"messageId":18,"value":{"intersections":[{"id":{"id":782},"laneSet":[{"connectsTo":[{"connectingLane":{"lane":11 ,"maneuver":"2000"},"signalGroup":2}],"laneAttributes":{"directionalUse":"80","laneType":{"vehicle":" 00"},"sharedWith":"1000"},"laneID":1,"maneuvers":"8000","nodeList":{"nodes":[{"delta":{"node-XY4":{"x ":2083,"y":-2129}}},{"delta":{"node-XY4":{"x":311,"y":-2532}}},{"delta":{"node-XY4":{"x":346,"y":-302 8}}},{"delta":{"node-XY1":{"x":0,"y":-305}}},{"delta":{"node-XY4":{"x":-122,"y":-2659}}}]}},{"connect sTo":[{"connectingLane":{"lane":7,"maneuver":"8000"},"signalGroup":2}],"laneAttributes":{"directional Use":"80","laneType":{"vehicle":"00"},"sharedWith":"1000"},"laneID":2,"maneuvers":"8000","nodeList":{ "nodes":[{"delta":{"node-XY4":{"x":638,"y":-2316}}},{"delta":{"node-XY4":{"x":337,"y":-2788}}},{"delt a":{"node-XY4":{"x":284,"y":-2729}}},{"delta":{"node-XY4":{"x":246,"y":-2732}}},{"delta":{"node-XY4": {"x":241,"y":-3344}}},{"delta":{"node-XY4":{"x":149,"y":-2739}}},{"delta":{"node-XY3":{"x":74,"y":-18 27}}},{"delta":{"node-XY6":{"x":352,"y":-11273}}}]}},{"connectsTo":[{"connectingLane":{"lane":8,"mane uver":"8000"},"signalGroup":2}],"laneAttributes":{"directionalUse":"80","laneType":{"vehicle":"00"}," sharedWith":"1000"},"laneID":3,"maneuvers":"8000","nodeList":{"nodes":[{"delta":{"node-XY4":{"x":998, "y":-2270}}},{"delta":{"node-XY4":{"x":309,"y":-2533}}},{"delta":{"node-XY4":{"x":322,"y":-3031}}},{" delta":{"node-XY4":{"x":244,"y":-2732}}},{"delta":{"node-XY4":{"x":242,"y":-3344}}},{"delta":{"node-X Y4":{"x":145,"y":-2739}}},{"delta":{"node-XY3":{"x":61,"y":-1523}}},{"delta":{"node-XY6":{"x":359,"y" :-11578}}}]}},{"connectsTo":[{"connectingLane":{"lane":9,"maneuver":"8000"},"signalGroup":2}],"laneAt tributes":{"directionalUse":"80","laneType":{"vehicle":"00"},"sharedWith":"1000"},"laneID":4,"maneuve rs":"8000","nodeList":{"nodes":[{"delta":{"node-XY4":{"x":1362,"y":-2222}}},{"delta":{"node-XY4":{"x" :319,"y":-2590}}},{"delta":{"node-XY4":{"x":322,"y":-3031}}},{"delta":{"node-XY4":{"x":242,"y":-2733} }},{"delta":{"node-XY4":{"x":242,"y":-3344}}},{"delta":{"node-XY4":{"x":146,"y":-2739}}},{"delta":{"n ode-XY3":{"x":51,"y":-1218}}},{"delta":{"node-XY6":{"x":366,"y":-11882}}}]}},{"connectsTo":[{"connect ingLane":{"lane":10,"maneuver":"8000"},"signalGroup":2}],"laneAttributes":{"directionalUse":"80","lan eType":{"vehicle":"00"},"sharedWith":"1000"},"laneID":5,"maneuvers":"8000","nodeList":{"nodes":[{"del ta":{"node-XY4":{"x":1724,"y":-2175}}},{"delta":{"node-XY4":{"x":324,"y":-2643}}},{"delta":{"node-XY4 ":{"x":321,"y":-3031}}},{"delta":{"node-XY4":{"x":270,"y":-3036}}},{"delta":{"node-XY4":{"x":215,"y": -3041}}},{"delta":{"node-XY4":{"x":148,"y":-2739}}},{"delta":{"node-XY3":{"x":73,"y":-1827}}},{"delta ":{"node-XY6":{"x":344,"y":-11273}}}]}},{"connectsTo":[{"connectingLane":{"lane":7,"maneuver":"4000"} ,"signalGroup":4}],"laneAttributes":{"directionalUse":"80","laneType":{"vehicle":"00"},"sharedWith":" 1000"},"laneID":6,"maneuvers":"4000","nodeList":{"nodes":[{"delta":{"node-XY2":{"x":-130,"y":-899}}}, {"delta":{"node-XY1":{"x":-296,"y":-72}}},{"delta":{"node-XY1":{"x":-303,"y":-14}}},{"delta":{"node-X Y1":{"x":-292,"y":69}}},{"delta":{"node-XY1":{"x":-225,"y":204}}},{"delta":{"node-XY1":{"x":-170,"y": 251}}},{"delta":{"node-XY1":{"x":-128,"y":276}}},{"delta":{"node-XY1":{"x":-100,"y":287}}},{"delta":{ "node-XY2":{"x":-151,"y":590}}},{"delta":{"node-XY1":{"x":-58,"y":299}}},{"delta":{"node-XY3":{"x":-2 35,"y":1814}}},{"delta":{"node-XY4":{"x":-371,"y":3332}}},{"delta":{"node-XY4":{"x":-310,"y":3339}}}, {"delta":{"node-XY4":{"x":-256,"y":3343}}},{"delta":{"node-XY4":{"x":-561,"y":3973}}}]}},{"laneAttrib utes":{"directionalUse":"40","laneType":{"vehicle":"00"},"sharedWith":"1000"},"laneID":7,"nodeList":{ "nodes":[{"delta":{"node-XY2":{"x":268,"y":470}}},{"delta":{"node-XY4":{"x":-312,"y":2419}}},{"delta" :{"node-XY3":{"x":-215,"y":1816}}},{"delta":{"node-XY4":{"x":-253,"y":2425}}},{"delta":{"node-XY4":{" x":-248,"y":2732}}}]}},{"laneAttributes":{"directionalUse":"40","laneType":{"vehicle":"00"},"sharedWi th":"1000"},"laneID":8,"nodeList":{"nodes":[{"delta":{"node-XY2":{"x":626,"y":522}}},{"delta":{"node- XY4":{"x":-494,"y":3932}}},{"delta":{"node-XY4":{"x":-287,"y":2728}}},{"delta":{"node-XY4":{"x":-247, "y":2732}}}]}},{"laneAttributes":{"directionalUse":"40","laneType":{"vehicle":"00"},"sharedWith":"100 0"},"laneID":9,"nodeList":{"nodes":[{"delta":{"node-XY3":{"x":988,"y":575}}},{"delta":{"node-XY4":{"x ":-314,"y":2418}}},{"delta":{"node-XY4":{"x":-312,"y":2726}}},{"delta":{"node-LatLon":{"lat":42519651 3,"lon":-830469748}}},{"delta":{"node-XY4":{"x":-217,"y":2429}}}]}},{"laneAttributes":{"directionalUs e":"40","laneType":{"vehicle":"00"},"sharedWith":"1000"},"laneID":10,"nodeList":{"nodes":[{"delta":{" node-XY3":{"x":1352,"y":628}}},{"delta":{"node-XY4":{"x":-315,"y":2418}}},{"delta":{"node-XY4":{"x":- 281,"y":2415}}},{"delta":{"node-XY3":{"x":-188,"y":1819}}},{"delta":{"node-LatLon":{"lat":425199014," lon":-830469603}}}]}},{"laneAttributes":{"directionalUse":"40","laneType":{"vehicle":"00"},"sharedWit h":"1000"},"laneID":11,"nodeList":{"nodes":[{"delta":{"node-XY3":{"x":1712,"y":681}}},{"delta":{"node -XY4":{"x":-276,"y":2116}}},{"delta":{"node-XY4":{"x":-349,"y":3028}}},{"delta":{"node-XY3":{"x":-155 ,"y":1516}}},{"delta":{"node-LatLon":{"lat":425199067,"lon":-830469158}}}]}}],"laneWidth":366,"refPoi nt":{"elevation":1879,"lat":425190000,"long":-830470000},"revision":1}],"layerID":1,"layerType":"inte rsectionData","msgIssueRevision":1}}}

## Slide 23: SPAT sample
{"Timestamp":1597167252195,"Direction":"RX","Message_id":19,"P1609dot2_flag":0,"Message":{"messageId" :19,"value":{"intersections":[{"id":{"id":782},"revision":4,"states":[{"signalGroup":1,"state-time-sp eed":[{"eventState":"stop-And-Remain","timing":{"maxEndTime":20294,"minEndTime":36001}}]},{"signalGro up":2,"state-time-speed":[{"eventState":"stop-And-Remain","timing":{"maxEndTime":20603,"minEndTime":2 0603}}]},{"signalGroup":3,"state-time-speed":[{"eventState":"stop-And-Remain","timing":{"maxEndTime": 20294,"minEndTime":36001}}]},{"signalGroup":4,"state-time-speed":[{"eventState":"permissive-Movement- Allowed","timing":{"maxEndTime":20545,"minEndTime":20545}}]},{"signalGroup":6,"state-time-speed":[{"e ventState":"stop-And-Remain","timing":{"maxEndTime":20294,"minEndTime":36001}}]},{"signalGroup":7,"st ate-time-speed":[{"eventState":"stop-And-Remain","timing":{"maxEndTime":20294,"minEndTime":36001}}]}, {"signalGroup":8,"state-time-speed":[{"eventState":"stop-And-Remain","timing":{"maxEndTime":20294,"mi nEndTime":36001}}]}],"status":"0080"}]}},"Version":"1.0"}

## Slide 24: BSM sample
{"Timestamp":1602096334182,"Direction":"RX","Message_id":20,"P1609dot2_flag":0,"Message":{"messageId":20,"value":{"coreData":{"accelSet":{"lat":-7,"long":24,"vert":-127,"yaw":-40},"accuracy":{"orientation":0,"semiMajor":5,"semiMinor":5},"angle":28,"brakes":{"abs":"engaged","auxBrakes":"unavailable","brakeBoost":"unavailable","scs":"engaged","traction":"engaged","wheelBrakes":"00"},"elev":1508,"heading ":1993,"id":"06230106","lat":425686803,"long":-829123338,"msgCnt":110,"secMark":34100,"size":{"length ":504,"width":196},"speed":0,"transmission":"park"},"partII":[{"partII-Id":0,"partII-Value":{"pathHis tory":{"crumbData":[{"elevationOffset":5,"latOffset":930,"lonOffset":742,"timeOffset":2230},{"elevati onOffset":9,"latOffset":930,"lonOffset":2164,"timeOffset":2610},{"elevationOffset":11,"latOffset":123 6,"lonOffset":2917,"timeOffset":2760},{"elevationOffset":11,"latOffset":8992,"lonOffset":9400,"timeOf fset":3600},{"elevationOffset":8,"latOffset":25129,"lonOffset":21801,"timeOffset":4780}]},"pathPredic tion":{"confidence":200,"radiusOfCurve":32767}}}]}},"Version":"1.0"}